## Slide 1
DAC programme
and
Interaction with ERTMS
Workshop ERA conference
Valenciennes, 23 April 2024

## Slide 2
Frédéric Henon
UIC
Johannes Gräber
Knorr-Bremse
Karel van Gils
EU-RAIL

## Slide 3: Agenda
Welcome and introduction 13:15 – 13:20
DAC, the bigger picture 13:20 – 13:40
    Organisation
    Planning
Interaction with ERTMS 13:40 – 14:30
    Operational rulebook
    Train length/-integrity
    Other interactions
Questions and discussion 14:30 – 14:45

## Slide 4
2. Digital automatic coupling (DAC),
the bigger picture

## Slide 5: The challenges for EU rail freight
Capacity
from bottleneck to green backbone
Productivity
from manual intervention to automation
Quality
from paper to digital
+ 50% rail freight
- 55% GHG emissions
by 2030
Courtesy of ÖBB
5

## Slide 6: Processes today – and tomorrow
manual freight wagon coupling
automatic freight wagon coupling
Courtesy of ÖBB
Courtesy of DAC4EU consortium
mechanical, pneumatical, energy & data coupling

## Slide 7: DAC core system & applications (Full Digital Freight Train Operations)
benefits = gains in the processes (time, system time, cost savings, capacity, reliability, quality, safety) + induced modal shift
DAC core system
Automated coupling & manual uncoupling and digital backbone
Recording of train composition
Automatic (in-train and remote) uncoupling
Heavier & longer trains (within existing infra limitations)
Increased payload
Increased speed via improved longitudinal forces
DAC train preparation
Automatic brake test & calculation of brake capacity
Automated technical wagon inspection
DAC shunting
Automated parking brake
Rear view camera for train driver
Proximity detection
Sound signals when train in motion
DAC train run
Train integrity, enabling ETCS L3 moving block operations
Increased speed via better braking performance
Multiple loco traction and trains up to 1500m
Derailment detection
DAC telematics (wagon & goods monitoring)
Predictive / preventive maintenance
detection of cargo condition
Cargo surveillance, intrusion alarm
Wagon data & loading information on mobile device
DAC loading & unloading
Automatic loading/unloading processes (replacement of hydr/pneum components, electro-mechanical actuators for bridge plates, automated cargo securing, heating elements for defrosting, …) via ext. energy supply
illumination for worker's safety & interior
red colour = components of the DAC basic package (only those use cases are linked to the pre-deployment trains)

## Slide 8: Preconditions for investing in DAC deployment (= everything that needs to be proven before investment decisions will be taken)
DAC-Technology (incl. additional DAC based technology) and DAC-operations/ functionalities are clearly defined (tech. package) and harmonised (Single European DAC System)
The technology meets all essential requirements - in particular in the area of RAMS (reliability-availability-maintainability-safety/security) - proven through large demonstrations
The operational functionalities/use cases bring the expected benefits - proven through large demonstrations incl. safety aspects
Positive CBA incl. adequate funding programs (by EU and MS) are made available and guaranteed
  to all European wagon and locomotive operators (RU) and keepers (as they will have to invest)
  in order to generate positive business cases in a maximum 10y perspective
  considering the individual/regional conditions such as the cases where upgrading is not possible/feasible
Simple, tailor-made “fast-lane” authorisation procedures are available & authorization risks are mitigated procedures for wagons and locos (incl. availability of relevant documentation)
A sound migration plan is set, guaranteeing simultaneous deployment in Europe (sector agreement and legal framework) based on available and adequate funding programs, established capacities for production and upgrading of wagons and locomotives, staff training, and availability of the necessary infrastructure and IT adaptations
2.
Proven technology
1.
Single European DAC system
3.
Proven operational functio- nality
4.
available adequate funding
6.
Sound migration plan
5.
Simple authorisation
DAC Deploy-ment
Precon- ditions for investing

## Slide 9: All DAC-related activities
Operating “100” DAC pre-deployment trains
Retrofitting plan
(traffic & customer sidings analysis, operational plan)
Infrastructural & IT adaptations
DAC/”Full Digital Freight Train Operations”
target operat. proc. functional requ’mts system architecture tech. development testing & demos tech. specification authoris. dossiers
Technology (mirroring & sector feedback)
Operational Procedures (mirroring & sector feedback)
FP 5 FDFTO sounding boards
Retrofit capacity plan (workshops, work-force, components)
Fleet Analyses & rtf Engineering (rtf readiness)
Placing into service plan (safety, workforce training, rulebooks etc.)
Investment plan & procurement framework plan
Funding & Financing plan
CBA (updates)
Other regulatory & legal framework plans
development of efficient & suitable authorisation process & requirements
preparing TSI drafts for the EC
Operational procedures standardization (plan & execution)
Technical harmonisation: preparing inputs for ERA TSI drafting process & driving EU standardisation
Alignment of rail & DAC system architecture
Executing European standardisation
TSI revision
Europe’s Rail Flagship Project 5
Europe’s Rail System Pillar
ESOs
EDDP
Stakeholder Management
EC/ERA
DAC migration roadmap

## Slide 10
DAC pre- deployment trains (100 in EU)
Technology Development
(incl. component testing and 4 demo trains)
(ER JU FP5 FDFTO + ER JU SP)
Determining milestone:
DAC Legal Package to be implemented before this deadline
Budget and resource need (already funded)
Major amendments/NEW:
DAC pilot deployment projects
DAC framework conditions development
Deployment Management Entity
10
The DAC General Master Plan 01 [June 2023]
existing
to be prepared
P
Deployment Management Entity
EXECUTION PHASE
€
€
Sector Statement
Funding Pilot Deployment Projects
DAC Legal Package:
TSIs final (technical + migration + operations)
Deployment Management Entity Deployment Funding Instrument
Suitable authorisation provisions
pre-deployment
deployment
deployment incl. procurement, preparation & ramp-up
Deployment Mgmt. Entity PREPARATION PHASE
€
Final validation & inclusion in TSIs
Ramp-up
DAC Migration Plan Development (EDDP)
€
€€
complete draft tech. specs
€
2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032/33?
Specific access to the network for commercial pilot test operations (based on draft technical specs)
Budget and resource need (currently mainly unfunded)
€
DAC framework conditions development
underway: CBA, suitable authorisation provisions, …
to be started: EU/MS policies, legal, funding, procurement, …
P
€
€€€€€

## Slide 11
Functions and components considered within the pre-deployment trains
The 100 pre-deployment trains shall be equipped with the DAC basic package:
DAC coupler incl. energy and data system
train composition detection
Automated brake test
Train integrity/train length determination
Automated uncoupling (in-train from loco)
  coupler with mechanical or push-button uncoupling from wagon side and including “prevent coupling” function
(Hybrid coupler for locos and DAC for special wagons, e. g. T3000 – if applicable)

## Slide 12
Why large-scale testing and a
pre-deployment phase is needed
Three objectives:
Ensure full reliability of the DAC technology
- Test DAC technology in commercial operations
- Assess the validity of assumptions developed in EDDP (Migration) / FP5 (Design)
- Assess technology integration by collaboration with FP5 technology providers and suppliers of existing assets
Prove added value and optimise EDDP processes for full DAC roll-out
- Gather information for full-scale deployment and roll-out
- Learn and develop. Create a steppingstone towards full DAC deployment
- inform and communicate with stakeholders
Ensure smooth integration of DAC into the overall railway system
- Ensure (mass) authorisation provisions can effectively be applied
- Test interchangeability/broad interoperability with other digital systems on trains, tracks and central IT systems
- Assess operational rules effectiveness
1
2
3

## Slide 13
3. Interaction with ERTMS
Operational rulebook
Train length/-integrity
Other interactions

## Slide 14
Operational DAC rulebook
From operational processes to a rulebook
Two examples of a DAC rulebook
Links between CCS/OPE based rulebooks and DAC rulebook

## Slide 15: From prelimniary operational procedures to a rulebook
How the processes in D2.1 are organized

## Slide 16: From preliminary operational procedures to a rulebook (2/2)
Last agreement on Rule Book Design :
Must be based on D2.1 but also next/other IP5 documents (i.e. D2.2, etc. ) and does not question the content
For the objective of pre-deployment trains, it will be based as first target on “EP” ERJU Processes (i.e. with no FDFT backend yet available)
In a further iteration, it will take into consideration the interaction with the FDFT System described in the “TP” Target Processes
It doesn’t describe at first stage all technical details, unless available (i.e.or push a button or to pull a lever)
It must describe Processes in a way that National Rules will no longer be necessary (nor allowed), and that the contents will be harmonized for all users and operators (Yard Manager, Shunting Operators, etc.) , still allowing adaptations due to geographical/local different organizational structures
The format will be aligned with Task 2 and finally agreed with ERA

## Slide 17: Two examples of a DAC rulebook
2 examples of Harmonized Operational Rules – general criterias
In both cases, considering that the content of D2.1 has already been validated, the processes are not re-evaluated nor re-discussed

## Slide 18: Two examples of a DAC rulebook (2/2)
Testing a Content Management System (CMS)
By using a Content Management System (CMS) it is be possible to manage both option (flowchart and textual), thus allowing the users of DAC/FDFT to choose the format they prefer for the rulebook: textual, flowchart, or both.
It is important to remark that the Operational Rules will have the same holistic approach of D2.1 and will thus be elaborated for all FDFTO actors.
The CMS will in any case allow the final users to distribute to specific roles only the rules that are applicable to them. It is also about readiness of digitalisation of Rule Book.

## Slide 19
Harmonized Operational Rules:
Creating links between T2 and T4
ERTMS and FDFTO scenarios are quite different, especially regarding the timeframe, but it’s possible to identify a common approach to similar topics
Three topics were discussed:
TSIs and Rulebook future developments
Examples of Rulebooks, scenario-based, and flow-chart based.
Relation between TSI and Rulebooks

## Slide 20: Link between Rulebooks T2 & T4 System Pillar
Scenario 101 perform Start of Mission
You are the driver of a train, and you will have to perform a Start of Mission
Enter the cab of the train
Open the cab by activating the power button / switch
- the automatic data entry is performed by the system
- all data is shown on de DMI in one overview
If all data are complete, start button is available, press start
If data is missing, press “main” on the DMI Menu, then “data entry” and submit the missing data
If all data are complete, start button is available, press start
Proceed with Scenario 102: departure
Text based
Flowchart based
SOM 101
Driver enters cab
Driver opens cab
Automatic data entry is performed
All data complete?
Input data manually
Start button available
Press start
n
y
Scenario based
20

## Slide 21
SOM 101
Example Task2:
Flow chart based
Text (instruction) based
Or both
Link between Rulebooks
21

## Slide 22: agreeing on a common target picture on the rulebook
Key statement :
We will make the DAC/FDFT Rule Book self-mandatory in Europe
22

## Slide 23
Safe Train length/-integrity

## Slide 24: Result of investigations of System Pillar Task 4
Through the work in Task 4, mainly regarding the high-level specifications and providing the system view, System Pillar will be supporting the improvement of freight train composition, operation and capacity of tracks.
Within this overall remit, an investigation on interfaces from train-internal (covered in full responsibility of FP5) to the “outside” world was conducted.
Regarding ERTMS, one major point was identified, to be covered by FA5: Enabling ETCS moving block operations (or L2 hybrid) of freight trains by delivering a Safe Train Length and Train Integrity.

## Slide 25: Recommendation by System Pillar Task 4
1
2
3
  Delivered through Polarion document “SPT4-WP3.1 FDFTO-ERTMS Trainlength/-integrity” to FP5 TRANS4M-R for consideration
  Basic concept:
  In addition to a continuous train integrity monitoring, 2 independent SIL 2 functions shall deliver a safe train length using 2 different type of information
  1 “merging function” (SIL 4) to achieve a SIL 4 information to be transferred to the trackside (as foreseen in TSI CCS SS 091 already)
1
2
3

## Slide 26: Current state of play in FP5 TRANS4M-R – realisation for “basic package” (= start of pre-deployment)
1
3
  Current concept:
  In addition to a continuous train integrity monitoring, only one SIL 2 function delivers a safe train length information
  The “merging function” to achieve a SIL 4 information to be transferred to the trackside shall be reached for the “target system” by combining the SIL 2 information provided by the FDFT system with a safe information from the train preparation process (decision also due to limiting the costs per wagon for the FDFT system)
  However, the FDFT system architecture, currently being described in FP5 D3.2, does not hinder to integrate a solution with two independent SIL 2 information from the FDFT system. If required, this approach could be developed at later stage, e.g. in FA5 CALL 2.
1
3
2
2
  Considering the high time pressure on pre-deployment trains, FP5 decided to concentrate on the following solution:

## Slide 27: Common understanding System Pillar / FP5
Flagship Area 5 is responsible to deliver a SIL 4 safe train length information to enable ETCS moving block (and L2 hybrid).
Common final target is to have a fully automated FDFTO system, therefore it is agreed, that in the end not to involve the driver in safety-related functions.
For the start of the pre-deployment, FP5 TRANS4M-R will realise one SIL 2 channel delivering a safe train length information (see slide before)
In parallel, 2 alternatives are further evaluated for the “target system” to provide a second SIL 2 information to be sent to the “merging function”
  The 2-channel in-train solution recommended by SP Task 4
  FDFT onboard or TCMS (both SIL 2) to receive from FDFT backend a parallel independent safe train length information

## Slide 28
3
Planning of System Pillar Task 2 and FP2 R2DATO to realise the “merging function”
  Current planning:
  Task 2 (in close cooperation with FP2, Task 4 and FP5) will issue a CR to include the “merging function” into the CCS onboard unit by September 2024
  Adaptation and entering into force of TSI CCS expected by 2027
  FP2 R2DATO to provide an onboard unit merging 2 independent SIL 2 functions of safe train length (provided by FA5) by 2026

## Slide 29
Other interactions ?

## Slide 30
4. Questions and Discussion

## Slide 31
Are you interested for further information?
Join the EDDP work packages and sounding boards: https://ec.europa.eu/eusurvey/runner/DACIdentificationGridforOperation
31

## Slide 32
Johannes.Graeber@knorr-bremse.com
Henon@uic.org
Karel.vangils@rail-research.europa.eu